## Slide 1: Hunter Expert Controller Qualification Seminar

## Slide 2
A
G
E
N
D
A
ACC99D Controller Hardware
ICORE/DUAL Controller Hardware
Station Output Hardware
System Diagnostics
2-Wire Field Components
Decoder Design
Installation Details
Installation Practices
Grounding Installation Details
ClikTM Sensor
Flow Sensors
Troubleshooting
Test

## Slide 3: Installation Practices

## Slide 4
Field / Controller Wiring

## Slide 5
Field / Controller Wiring

## Slide 6: ACC Installation Details

## Slide 7
ACC Installation Details

## Slide 8
ACC Installation Details

## Slide 9
ACC Installation Details

## Slide 10
ACC Installation Details

## Slide 11
ACC Installation Details

## Slide 12: ACC Electrical Details

## Slide 13
ACC Transformer

## Slide 14
ACC Transformer

## Slide 15
ACC Transformer
The green, or green-and-yellow safety ground (service ground) is not required or permitted with this floating ground, double-insulated transformer.

## Slide 16: ACC Controller Components

## Slide 17
5
8
7
0
0
0
ACC Transformer

## Slide 18
Primary Power Connection Compartment
Secondary Power Connection Compartment
115Vac, 230Vac/240Vac
Hot and Neutral, NO Ground
24Vac @ 4 Amp. = Yellow
7Vac @ 3.4 Amp. = Red
Controller Fuse (1/4 Turn)
2 Amp. @ 250V Fast Blow
5 X 20 mm
ACC Transformer

## Slide 19
5
7
2
0
0
0
ACC Master Module

## Slide 20
F
I
R
M
W
A
R
E
2.02.017 24Vac
4.22.010 IMMS-ET
5.23.008 SolarSync
ACC Master Module

## Slide 21
IMMS ET / SolarSync Connections
ACC Master Module
24Vdc – 19Vdc Minimum

## Slide 22
ACC Master Module
Flow Sensor Connections
24Vdc – 19Vdc Minimum
HFS or 200 Series Badger Flow Sensors

## Slide 23
ACC Master Module
Clik™ Sensor Connections
Normally Closed Circuits

## Slide 24
ACC Master Module
24Vac Power Connection
400Ma (PTC protected)
~Positive Temperature Coefficient~

## Slide 25
ACC Master Module
P/MV1 and P/MV2 Connections
0.32 Amp @ 24Vac

## Slide 26
ACC Master Module
P/MV1 and P/MV2 on Power-up
Flashing = Communications

## Slide 27
ACC Master Module
Green = Active, no Over-currents
P/MV1 and P/MV2 when Active

## Slide 28
ACC Master Module
P/MV1 and P/MV2 when Over-current
Flashing Red = Overcurrent

## Slide 29
5
7
1
5
0
0

## Slide 30
F
I
R
M
W
A
R
E
1009BFF 24Vac
2.00.25 Decoder
3.01.00 IMMS Central
3.12.02 Sensor Decoder
4.01.03 IMMS-ET
5.01.002 SolarSync
571500 ~ ACC Facepack

## Slide 31
P
R
O
G
R
A
M
571500 ~ ACC Facepack

## Slide 32
A
C/G
M
6
0
0
ACC Station Modules
ACM-600
AGM-600

## Slide 33
F
I
R
M
W
A
R
E
1.03.003 Original
1.04.001 Increased Holding
Current
2.01.005 Enhanced
Diagnostics
ACC Station Modules

## Slide 34
ACC Station Modules
ACC Station Modules
6-Station, Standard Lightning Protection
6-Station, Heavy-Duty Lightning Protection
ACM-600
AGM-600

## Slide 35
ACC Station Modules
ACC Station Modules
ACM-600
AGM-600
0.56 Amp @ 24Vac

## Slide 36
Station Outputs when Active
Green = Active, no Over-currents
ACC Station Modules
0.56 Amp @ 24Vac

## Slide 37
Flashing Red = Overcurrent
Station Outputs when Over-current
ACC Station Modules

## Slide 38
Red LED Indicators
Station Outputs During Power-up
ACC Station Modules
1.
0
3.
0
0
3
1.
0
4.
0
0
1
2.
0
1.
0
0
5

## Slide 39
A
D M 9
9
ACC Decoder Module

## Slide 40
F
I
R
M
W
A
R
E
1.02.003 Original
2.00.020 Enhanced
Communications
2.00.024 Enhanced
Diagnostics
ADM-99

## Slide 41
ADM-99
Decoder
Programming
Port
Multiple
2-Wire
Paths
Decoder Module
Indicator LEDs

## Slide 42
Decoder Fault
Module/Line Activity
Line Status
Communicating
Blank / OFF = Normal, All is good
Steady RED = ADM Problem
Blinking RED = Solenoid Shorted /
No Decoder Comm
ADM-99

## Slide 43
Decoder Fault
Module/Line Activity
Line Status
Communicating
Blank / OFF = Normal, No Irrigation
Steady RED = ADM Problem
Blinking RED = Solenoid Short /
No Decoder Comm
Blinking Green = Irrigating Station
ADM-99

## Slide 44
Decoder Fault
Module/Line Activity
Line Status
Communicating
Blank / OFF = No Communications
Blinking Amber = Programming Port
Communications
Blinking Green = 2-Wire Path Communications
ADM-99

## Slide 45
Decoder Fault
Module/Line Activity
Line Status
Communicating
Blank / OFF = ADM Problem
Steady Green = Normal, All is Good
Blinking Green = ADM Problem
ADM-99

## Slide 46
2 solenoids per output
ICD Decoders
2-way communications
Flow/Clik sensor decoder
Surge protection on each decoder
1, 2, 4, 6 station decoder

## Slide 47
170
Q & A

## Slide 48: ICORE Installation Details

## Slide 49
ICORE Installation Details

## Slide 50
ICORE Installation Details

## Slide 51
ICORE Installation Details

## Slide 52
ICORE Installation Details

## Slide 53
ICORE Installation Details

## Slide 54: ICORE Electrical Details

## Slide 55
1
5
4
6
2
8
Primary Power Connection Compartment
Secondary Power
115Vac, 230Vac/240Vac
Hot, Neutral and Ground
24Vac @ 1.6 Amp. = Yellow
ICORE Transformer

## Slide 56
ICORE Transformer

## Slide 57
ICORE Transformer

## Slide 58: ICORE Controller Components

## Slide 59
M
A
S
T
E
R
M
O
D
S
141700 (Metal)
121405 (Plastic)
ICORE Master Modules

## Slide 60
141700
(Metal)
121405
(Plastic)
ICORE Master Modules

## Slide 61
ICORE Controllers
c
c
P/MV
REM
AC1
AC2
GND
S1
S2
S3
S1
S2
S3
c
24 Vac Power Connections

## Slide 62
ICORE Controllers
c
c
P/MV
REM
AC1
AC2
GND
S1
S2
S3
S1
S2
S3
c
Clik™ / Flow Sensor Connections
(Normally Closed Circuits)

## Slide 63
ICORE Controllers
c
c
P/MV
REM
AC1
AC2
GND
S1
S2
S3
S1
S2
S3
c
Field Commons Connections

## Slide 64
ICORE Controllers
c
c
P/MV
REM
AC1
AC2
GND
S1
S2
S3
S1
S2
S3
c
Pump/Master Valve Connections

## Slide 65
1
2
4
7
0
5

## Slide 66
F
I
R
M
W
A
R
E
1.00.XX 24Vac
2.00.10 Decoder/Flow
3.00.XX SolarSync/VFD Pump
124705 ~ ICORE Facepack
(2.00.12)

## Slide 67
P
R
O
G
R
A
M
124705 ~ ICORE Facepack

## Slide 68
I
C
M
6
0
0
ICORE Station Modules

## Slide 69
ICORE Station Modules
0.56 Amp @ 24Vac

## Slide 70
D
U
A
L
DUAL 48 Module

## Slide 71
DUAL 48 Module
Solenoid chatter
Line amperage indicator (500mA Max.)
Active station status
Line status indicator
Stations on decoder module

## Slide 72
DUAL 48 Module

## Slide 73
2 solenoids per output
DUAL 48 Module
Multiple same station addresses
2 station decoder
Surge decoder
1 station decoder

## Slide 74
170
Q & A

## Slide 75: 2-Wire Field Components

## Slide 76
IDWIRE: The Magic in the Wire
IDWire: Twisted, red/blue, direct burial in flexible colored jacket
Color coding for correct installation & tracing
Jacketed for better protection
Twisted-pair design provides:
  Greater surge resistance
  Greater tensile strength
  Resistance to electrical noise and crosstalk from AC wiring.
2-Wire Field Components

## Slide 77
DS-
DS Type
Connectors
(Decoder - Solenoid)
3M DBY/R-6
Connectors
(2-wire - Decoder)
Wire Connectors
2-Wire Field Components

## Slide 78
Grounding Plates
Grounding Plate
Installed
Grounding Plate
4” x 36” / 4” x 96”
10cm X 1m / 10cm x 2.4m
2-Wire Field Components

## Slide 79
Grounding Extras
Cadweld
Plus
Power Set TM
2-Wire Field Components

## Slide 80
Paige Wire 270DCFD
2-Wire Field Components

## Slide 81: Decoder Design

## Slide 82: Planning Your 2-wire Paths
P
L
A
N
N
I
N
G

## Slide 83
Each 2-wire cable output is called a “path”.
All decoder stations MAY be on a single path. (Not recommended)
There are multiple paths available from the controller.
Use as many paths as you need, to reach all valves efficiently.
Paths are not to be “looped” back to controller, or each other.
Path
Decoder Design
Planning your 2-wire paths

## Slide 84
Decoder Design
Place a decoder by each 24VAC valve (standard solenoids) (A few solenoids with internal diodes or capacitors may not be decoder compatible, but most are)
Max distance from controller to furthest decoder on each path: (Follow Manufacturer's specs.)
Max distance from decoder to solenoid, 150 ft. (Recommended maximum)
= Decoder
= Earth Ground
Planning your 2-wire paths

## Slide 85
Use a different color cable for each wire path
2-wire paths can be spliced
  Follow the splicing rules
  Use pipe trenches to route wires
Maximum wire distance applies to each wire path from the controller to the end of each run
= Decoder
= Earth Ground
Decoder Design
Planning your 2-wire paths

## Slide 86: Decoder Path Wire Sizing
W
I
R
E
S
I
Z
I
N
G

## Slide 87
Decoder Design
Wire Sizing
DUAL 5,000 ft / 1.5 km
DUAL 7,500 ft / 2.25 km

## Slide 88
Decoder Design
Lw = Wire path length in feet or meters
2 x Vd x 1,000
Rw x Iw
Lw =
Vd = Allowable voltage drop
Rw = Resistance per 1,000ft / 1,000m of wire
Iw = Maximum current on 2-wire path
Wire Sizing

## Slide 89
Decoder Design
Vd = Allowable voltage drop
(1.4 x 24) – 20 = 14V
Wire Sizing

## Slide 90
Decoder Design
Rw = Resistance of wire
Wire Sizing

## Slide 91
Decoder Design
Iw = Maximum current on 2-wire path
Decoders at idle, no solenoids active = 3.5mA (designated by 0.005)
Decoders Active, 1 Hunter solenoid = 45mA (designated by 0.045)
There are two currents to calculate;
Wire Sizing

## Slide 92
Decoder Design
Wire Sizing

## Slide 93
170
Q & A

## Slide 94: Decoder Component Installation
I
N
S
T
A
L
L
A
T
I
O
N

## Slide 95
Decoder Design
Decoder Component Installation
3’ Wire Slack for Service

## Slide 96
Decoder Design
Single Station Decoder
Decoder Component Installation

## Slide 97
Decoder Design
Multiple Station Decoder
Decoder Component Installation

## Slide 98
Decoder Design
Decoder Grounding
Decoder Component Installation

## Slide 102: Decoder Programming at Controller
P
R
O
G
R
A
M
M
I
N
G
Decoder Programming with ICD-HP
ACC

## Slide 103
Decoder Design
ACC Decoder Programming at Controller
Use the programming port on the ADM99
Do NOT use the same station number on multiple decoders
Multiple station decoders program stations sequentially
Any station decoder can be programmed as a Pump/Master Valve
Sensor decoders can be programmed as a Clik and/or Flow sensor
Sensor decoders programmed for flow use sensor address #5

## Slide 104
F
I
R
M
W
A
R
E
Decoder Programming
(Hands On)
Decoder Design
Decoder Programming at Controller

## Slide 105
Decoder Design
Decoder Programming with ICD-HP
Can use the power from the 2-wire path or ICD-HP
Do NOT use the same station number on multiple decoders
Multiple station decoders program stations individually
Any station decoder can be programmed as a Pump/Master Valve
Sensor decoders can be programmed as a Clik and/or Flow sensor
Sensor decoders programmed for flow use sensor address #5

## Slide 106
F
I
R
M
W
A
R
E
ICD-HP Programming
(Hands On)
Decoder Design
Decoder Programming with ICD-HP

## Slide 107: Decoder Programming at Controller
P
R
O
G
R
A
M
M
I
N
G
Decoder Programming with ICD-HP
DUAL

## Slide 108
Decoder Design
DUAL Decoder Programming at Controller
Use the programming port on the DUAL
Using the same station number on multiple decoders
Multiple station decoders program stations sequentially
Multiple station decoders program stations non-sequentially
NO Pump/Master Valve decoders
NO Sensor decoders on the DUAL system

## Slide 109
F
I
R
M
W
A
R
E
Decoder Programming
(Hands On)
Decoder Design
DUAL Decoder Programming at Controller

## Slide 110
Decoder Design
DUAL Decoder Programming at Controller
Use the programming port on the DUAL
Using the same station number on multiple decoders
Multiple station decoders program stations sequentially
Multiple station decoders program stations non-sequentially
NO Pump/Master Valve decoders
NO Sensor decoders on the DUAL system

## Slide 111
F
I
R
M
W
A
R
E
ICD-HP Programming
(Hands On)
Decoder Design
DUAL Decoder Programming at Controller

## Slide 112
G
R
O
U
N
D
I
N
G
At the Controller
At the First 2-wire connection
At the End of every 2-wire path
Every 12TH decoder
Every 1,000’ / 300 m
Decoder Design

## Slide 113
0
1
0
2
0
3
0
4
0
5
0
6
0
7
0
8
0
9
1
0
1
1
1
2
Minimum Grounding
Decoder Design
Every 12TH Decoder /
End of 2-wire Path

## Slide 114
0
1
0
2
0
3
0
4
0
5
0
6
0
7
0
8
0
9
1
0
1
1
1
2
1,000 Feet
300 Meters
Decoder Design
First 2-wire
Connection
Minimum Grounding

## Slide 115
0
1
0
2
0
3
0
4
0
5
0
6
0
7
0
8
0
9
1
0
1
1
1
2
1,000 Feet
300 Meters
Decoder Design
10 Ohms
Or Less
Minimum Grounding

## Slide 116
0
1
0
2
0
3
0
4
0
5
0
6
0
7
0
8
0
9
1
0
1
1
1
2
Decoder Design
Grounding Principle

## Slide 117
0
1
0
2
0
3
0
4
0
5
0
6
0
7
0
8
0
9
1
0
1
1
1
2
Decoder Design
Grounding Principle

## Slide 118
170
Q & A

## Slide 119: Grounding Installation Details

## Slide 120
Grounding Installation Details
Grounding Rod
L
Grounding Rod
2xL
Ground Rod sphere of influence

## Slide 121
Grounding Installation Details
W
3xW
Grounding Plate
Ground Plate sphere of influence
3xL
L
Grounding Plate

## Slide 122
Grounding Installation Details
Up to 64 Stations, Non-rocky soils

## Slide 123
Grounding Installation Details
Up to 64 Stations, all soils

## Slide 124
Grounding Installation Details
Up to 96 Stations, Non-rocky soils

## Slide 125
Grounding Installation Details
Up to 96 Stations, all soils

## Slide 126
Grounding Installation Details
Up to 128 Stations, Non-rocky soils

## Slide 127
Grounding Installation Details
Up to 128 Stations, all soils

## Slide 128
Grounding Installation Details
Up to 256 Stations, all soils

## Slide 129
170
Q & A

## Slide 130: ClikTM Sensors

## Slide 131
C
L
I
K
S
E
N
S
O
R
ACC
ICORE

## Slide 132
F
I
R
M
W
A
R
E
ClikTM Sensor Programming
(Hands On)
ClikTM Sensor

## Slide 133: Flow Sensors

## Slide 134
F
L
O
W
S
E
N
S
O
R
ACC
ICORE

## Slide 135
Flow Sensor Installation
Minimum Distance
10 x Pipe size
Minimum Distance
5 x Pipe size
FLOW
FLOW
Flow Sensor
Fitting

## Slide 136
F
I
R
M
W
A
R
E
Flow Sensor Programming
(Hands On)
Flow Sensor

## Slide 137
170
Q & A

## Slide 138: Troubleshooting Notes

## Slide 139
T
R
O
U
B
L
E
S
H
O
O
T
I
N
G
Wire Size Calculation
Wire Resistance
Component Amperages
Tools

## Slide 140
T
O
O
L
S
Pro93 V.O.M.
Wire Tracker
Ground Fault Locator
Misc. hand tools
Test solenoid
Troubleshooting Tools

## Slide 141
F
I
R
M
W
A
R
E
Pro93 V.O.M.
(Hands On)
Troubleshooting Tools

## Slide 142
170
Q & A

## Slide 143
24VAC Controller
120VAC
(60Hz)
24-26VAC
(60Hz)
24Vac Vs Decoder

## Slide 144
0 Volts
+26 Volts
-26 Volts
60Hz
(Hertz is equivalent to cycles per second)
1/60 Second
24Vac Vs Decoder
24Vac Sine Wave

## Slide 145
24Vac Vs Decoder
24Vac Sine Wave

## Slide 146
Controller
Valves
Wiring
24Vac Vs Decoder

## Slide 147
Decoder Controller
120VAC
(60Hz)
30-35VDC (+/- pulsing)
(1 – 2 Hz)
24Vac Vs Decoder

## Slide 148
0 Volts
+38 Volts
1Hz
(Hertz is equivalent to cycles per second)
1 Second
-38 Volts
24Vac Vs Decoder
Square Wave

## Slide 149
0 Volts
+38 Volts
1 Second
Data Signal
-38 Volts
24Vac Vs Decoder
Square Wave

## Slide 150
24Vac Vs Decoder
Square Wave

## Slide 151
Decoders
Grounding
Controller
Valves
Wiring
Pulsing 30-38Volts
Data Signals
24Vac Vs Decoder

## Slide 152
11VAC – 13VAC
30-38V
1Hz
500Hz
Constantly “HOT”
and pulsing
D
E
C
O
D
E
R
24Vac Vs Decoder

## Slide 153
24Vac Vs Decoder
Decoder to Solenoid

## Slide 154
T
O
O
L
S
Fluke 117 Voltmeter
Extech Clamp On mA meter
ICD-HP
Armada Wire Tracker
Armada Ground Fault Locator
Misc. hand tools
24Vac/60Hz power source
Test decoder/solenoid
Troubleshooting Tools
Armada Clamp On mA meter

## Slide 155
FLUKE 117 Voltmeter
Troubleshooting Tools

## Slide 156
Extech 380942
Troubleshooting Tools

## Slide 157
Armada Pro93
Troubleshooting Tools

## Slide 158
Hunter ICD-HP Features
Decoder Programming
Decoder Firmware
Diagnostics
Station Test
Clik/Flow Sensor Test
Volt / Amp Meter
Hunter ICD-HP
Troubleshooting Tools

## Slide 159
Miscellaneous Tools
Troubleshooting Tools

## Slide 160
24Vac, 60Hz power source
Troubleshooting Tools

## Slide 161
Test Decoder/solenoid
Troubleshooting Tools

## Slide 162
Pro300 Tracker
Diagnostic Tools

## Slide 163
GFL3000 Ground Fault Locator
Troubleshooting Tools

## Slide 164
Extech 382153
Troubleshooting Tools

## Slide 165
DS-
DS Type
Connectors
(Decoder - Solenoid)
3M DBY/R-6
Connectors
(2-wire - Decoder)
Wire Connectors
Troubleshooting Tools

## Slide 166
S
Y
S
T
E
M
C
O
M
P
O
N
E
N
T
S
Controller
2-Wire Path
Decoder
Solenoid
System Diagnostics

## Slide 167
Controller
Field Wiring (2-wire path)
Decoder
Solenoid
System Diagnostics

## Slide 168
What are the alarms or fault indicators?
  Controller related?
  2-wire related?
  Decoder related?
  Solenoid related?
System Diagnostics

## Slide 169
C
O
N
T
R
O
L
L
E
R
System Diagnostics
Controller
2-Wire Path
Decoder
Solenoid

## Slide 170
Check programming !
Check the decoder set-up!
Check sensor set-up !
Check the LED indicators on the ADM.
Check the LED indicators on the Master Module
Check the 2-wire path voltage at the controller
Check the controller using a test decoder/solenoid.
System Diagnostics
Controller

## Slide 171
Controller
System Diagnostics
No status light on the ADM (2-wire path);
  Power bar in the “OFF” position
  Decoder module
  Master module
MV1/MV2 LEDs continuously cycle;
  No station/decoder modules installed
  Station module
  Master module
  Face pack
Transformer fuse continuously blows;
  High voltage wire shorting out (120/230)
  Decoder module (2-wire path)
  Master module

## Slide 172
System Diagnostics
Using a Fluke 117

## Slide 173
System Diagnostics
Using a ICD-HP

## Slide 174
System Diagnostics
Using a test decoder/solenoid

## Slide 175
2
W
I
R
E
P
A
T
H
System Diagnostics
Controller
2-Wire Path
Decoder
Solenoid

## Slide 176
Check 2-wire Resistance.
  Resistance should be 600,000 ohms or greater.
Check 2-wire Voltage.
Voltages should be 20V – 35V
(Using the controller voltage)
Wire splices must be done with the manufacturer’s specified connectors (3M, DBY/R-6 on 2-wire path)
Trace out the 2-wire path (Pro300 Tracker)
Check the 2-wire path for a leak to ground (GFL3000)
System Diagnostics
2-wire Path

## Slide 177
DS Type
Connectors
(wrong application)
System Diagnostics
2-wire Path
Good connector in the wrong application !

## Slide 178
System Diagnostics
2-wire Path

## Slide 179
170
Q & A

## Slide 180: Diagnostic Method
2
W
I
R
E
P
A
T
H

## Slide 181
System Diagnostics
2-wire Path
Half Method;
  Test at the controller
  Test at the first connection from the controller
  Test at the next connection or “Half” way down the 2-wire path
  Test at the next connection or “Half” way down the 2-wire path
  Continue this until you have pin-pointed the damaged area/component

## Slide 182: Overload / Resistance
2
W
I
R
E
P
A
T
H

## Slide 183
System Diagnostics
2-wire Path
2-wire path shorted (ADM Overload);
RESISTANCE !!!
  Test at the controller
  Test at the first connection from the controller
  Test at the next connection or “Half” way down the 2-wire path
  Test at the next connection or “Half” way down the 2-wire path, towards the short
  Continue this until you have pin-pointed the damaged area/component

## Slide 184
System Diagnostics
Remove all 2-wire
paths from the
ADM99 and check
resistance on the
2-wire paths
2-wire Path – Half Method
37 Ohms
600,000+ Ohms
600,000+ Ohms
600,000+ Ohms

## Slide 185
System Diagnostics
Break 2-wire path
at first connection
2-wire Path – Half Method

## Slide 186
System Diagnostics
Re-check the
resistance of the
2-wire path.
2-wire Path – Half Method
600K+ Ohms

## Slide 187
System Diagnostics
Check resistance
here both pairs,
mark controller side
wires
37 Ohms
600K+ 0hms
2-wire Path – Half Method
Problem Direction

## Slide 188
System Diagnostics
Resistance on the 2-wire path
2-wire Path – Half Method

## Slide 189
System Diagnostics
Break 2-wire path
at connection
2-wire Path – Half Method
600K+ Ohms

## Slide 190
System Diagnostics
Check resistance
here on the “field”
side wires
600K+ Ohms
2-wire Path – Half Method
600K+ Ohms

## Slide 191
System Diagnostics
Twist the Red/Blue
“field” side wires
together
2-wire Path – Half Method
600K+ Ohms

## Slide 192
System Diagnostics
2-wire Path – Half Method
1-3 Ohms
600K+ Ohms
Problem Direction
Check resistance
here on all wires
37 Ohms

## Slide 193
System Diagnostics
Untwist Red/Blue
wires and reconnect
paths together
2-wire Path – Half Method

## Slide 194
System Diagnostics
2-wire Path – Half Method
600K+ Ohms
600K+ Ohms
Break 2-wire path
at connection
37 Ohms
Half way point or
Next 2-wire spice

## Slide 195
System Diagnostics
2-wire Path – Half Method
37 Ohms
Check resistance
here on the “field”
side wires

## Slide 196
System Diagnostics
2-wire Path – Half Method
37 Ohms
Check resistance
here on the
2-wire paths
37 Ohms
600K+ Ohms

## Slide 197
System Diagnostics
2-wire Path – Half Method
37 Ohms
37 Ohms
600K+ Ohms
Twist the Red/Blue
“field” side wires
together

## Slide 198
System Diagnostics
2-wire Path – Half Method
Check resistance
here on the
2-wire paths
37 Ohms
600K+ Ohms
1-3 Ohms
37 Ohms
1-3 Ohms

## Slide 199
170
Q & A

## Slide 200: Voltage
2
W
I
R
E
P
A
T
H

## Slide 201
System Diagnostics
2-wire path damaged;
VOLTAGE !!!
  Test the voltage at the controller/ADM99
  Test at the first connection from the controller
  Test at the next connection or “Half” way down the 2-wire path
  Test at the next connection or “Half” way down the 2-wire path
  Continue this until you have pin-pointed the damaged area/component

## Slide 202
System Diagnostics
2-wire Path – Half Method
Check the
voltage of the
2-wire path.
33.54Volts

## Slide 203
System Diagnostics
2-wire Path – Half Method
Check the
voltage of the
2-wire path.
33.54Volts

## Slide 204
System Diagnostics
2-wire Path – Half Method
Check the
voltage of the
2-wire path.
33.54Volts

## Slide 205
System Diagnostics
2-wire Path – Half Method
Check the
voltage of the
2-wire path.
Half way point or
Next 2-wire spice
0 Volts

## Slide 206
System Diagnostics
2-wire Path – Half Method
Check the
voltage of the
2-wire path.
33.54Volts
0 Volts

## Slide 207
System Diagnostics
2-wire Path – Half Method
Check the
voltage of the
2-wire path.
0 Volts
33.54Volts
Damaged
Area

## Slide 208
System Diagnostics
2-wire Path
Voltage 2-wire path

## Slide 209
System Diagnostics
2-wire Path
Voltage 2-wire path (field side)

## Slide 210
System Diagnostics
2-wire Path
Voltage 2-wire path (controller side)

## Slide 211
170
Q & A

## Slide 212: Amperage
2
W
I
R
E
P
A
T
H

## Slide 213
System Diagnostics
2-wire Path
Amperage 2-wire path (controller power)

## Slide 214
2-wire Path
Connecting the 24Vac power source

## Slide 215
System Diagnostics
2-wire Path
Using a Extech 380942 with 24Vac power

## Slide 216
System Diagnostics
Using a Extech 380942 with 24Vac power
NO VOLTAGE !!
2-wire Path

## Slide 217
1
2
3
4
5
6
7
8
9
10
11
12
13
14
19
18
17
16
15
24
23
22
21
20
28
27
26
25
217mA
108.5mA
54mA
24Vac
Power
Supply
Each decoder (7.75mA @ 24Vac)
2-wire Path
System Diagnostics

## Slide 218
1
2
3
4
5
6
7
8
9
10
11
12
13
14
16
15
7.75mA
47mA
17
18
20
22
23
24
25
26
28
27
19
21
54mA
47mA
217mA
194mA
24Vac
Power
Supply
2-wire Path
System Diagnostics

## Slide 219
1
2
3
4
5
6
7
8
9
10
11
12
13
14
16
15
17
18
20
22
23
24
25
26
28
27
19
21
24Vac
Power
Supply
2-wire Path
System Diagnostics

## Slide 220
170
Q & A

## Slide 221
D
E
C
O
D
E
R
System Diagnostics
Controller
2-Wire Path
Decoder
Solenoid

## Slide 222
Decoder Diagnostics;
Check the wire connections on the suspect decoder
Check the temperature of the suspect decoder
Activate the decoder/solenoid with the ICD-HP
Check the decoder amperage draw (7.75mA at 24Vac)
Check and confirm that the decoder address is correct in the controller
Install your test decoder
Activate test decoder from the controller
System Diagnostics
Decoder

## Slide 223
S
O
L
E
N
O
I
D
System Diagnostics
Controller
2-Wire Path
Decoder
Solenoid

## Slide 224
Solenoid Diagnostics;
Check the wire connections on the suspect solenoid.
Check the solenoid amperage (45mA)
Check and confirm that the decoder address is correct in the controller !
Activate decoder/solenoid with a ICD-HP
Install a new solenoid.
Activate decoder/solenoid from the controller.
System Diagnostics
Solenoid

## Slide 225
170
Q & A

## Slide 226: Test